## Slide 1
Phytotechnology in the Present and Future: Remedies for Contaminated Soil and Water
Alain Manceau
http://isterre.fr/alain-manceau
Seminar given at the University of Notre Dame in the Department of Civil & Environmental Engineering & Earth Sciences on the invitation of Dr. Patricia A. Maurice - April 18, 2013
Challenges and Innovation in Civil and Environmental Engineering
Notes: The term “phytotechnology” refers to scientific and engineering solutions involving plants and associated miroorganisms to clean and protect environmental matter contaminated by trace elements (TEs), typically metals (TMs), metalloids, radionuclides, and/or organic xenobiotics (OX).

## Slide 2
Rhizosphere
Introduction
Absorption
Secretion
Respiration
K, nitrate, phosphate
H+/OH-
Organics
CO2
O2
Bulk soil
Notes: At the heart of phytotechnology is the rhizosphere which is the interface between the contaminated compartment and the “cleaning factory”, which is the plant. The rhizosphere is the narrow region of soil that is directly influenced by root secretions and associated soil microorganisms. Soil which is not part of the rhizosphere is known as bulk soil. Plants secrete many compounds into the rhizosphere which serve different functions (sugars, proteins).

## Slide 3
Rhizosphere
Introduction
Absorption
Secretion
Respiration
K, nitrate, phosphate
H+/OH-
Organics
CO2
O2
Bulk soil

## Slide 4
Rhizosphere
Introduction
Absorption
Secretion
Respiration
K, nitrate, phosphate
H+/OH-
Organics
CO2
O2
Bulk soil
Notes: Most plants live in symbiosis with fungal myccorhizae, which extend the influence volume of the plant activity.

## Slide 5
Mycorhizosphere
Introduction
Absorption
Secretion
Respiration
K, nitrate, phosphate
H+/OH-
Organics
CO2
O2
Bulk soil

## Slide 6
Introduction
Notes: Example of mycorrhiza

## Slide 7
Introduction
Phragmites australis
(common reed)
Notes: P. Australis is a large perennial grass found in wetlands throughout temperate and tropical regions. It is one of the main wetland plant species used in phytoremediation. The soil matrix can be totally « rhizospheric ».

## Slide 8
Phytotechnologies
  Phytostabilization
  Rhizofiltration
  Phytolixiviation
  Phytoextraction
  Phytovolatilization
Cross-disciplinary field:
Agronomy
Soil science
Bio(geo)chemistry
Environmental mineralogy
Plant biology
Plant genetics
Pilon-Smits, Ann. Rev. Plant Biol., 2005.

## Slide 9
Involves the reduction of the mobility of trace metals (TMs) in soil with amendments to minimize TMs transfer to the food chain and leaching to goundwater. In situ treatment.
Phytostabilization
Principle :
Solubility (log Ksp)
-7.8
-12.8
-27.5
-76.8
-82.3
-84.4
-99.1
-99.3
-112.6
Anglésite - PbSO4
Cerrusite - PbCO3
Galène - PbS
Fluoropyromorphite - Pb5(PO4)3F
Hydroxypyromorphite - Pb5(PO4)3OH
Chloropyromorphite - Pb5(PO4)3Cl
Hinsdalite - PbAl3(PO4)(OH)6SO4
Plumbogummite - PbAl3(PO4)2(OH)5H2O
Corkite - PbFe3(PO4)(OH)6SO4
Mineral
Solubility ↔ Bio-disponibility ↔ Toxicity
Phosphate added to lead-contaminated soil
Notes: This phytotechnology works pretty well for Pb owing to the low solubility of lead phosphates, and also for Cr (reduction of mobile Cr(VI) to immobile Cr(III)) and for radionuclides.

## Slide 10
Before…
After phytostabilization
TMs are mobile, hence phytotoxic.
Site: Lommel, Belgium.
TMs are still present, but immobile, allowing the reinstallation of a vegetation cover and the further development of crops.
Vangronsveld et al., Environ. Pollution, 1995.
Contamination source: Zn smelter
Phytostabilization
Festuca rubra
Agrostis capillaris
Zn, Cd, Pb
Application :
(Re)-vegetation of large-scale areas (barren land, mine spoils, abandoned smelter…).
[Zn] = 3%
Notes: This technique can be used to create an ecosystem of indigenous flora and fauna, thus restoring the ecological value of the site.

## Slide 11
Revegetation the 1st yr. with Holcus lanatus and the 2nd yr. with Pinus pinaster after in situ As inactivation by the co-amendment of zerovalent Fe, coal fly ash, and compost.
Mench et al., Plant & Soil, 2003.
Before…
[As] = 0.13%
Phytostabilization
Contamination source: Au mine
Application :
(Re)-vegetation of large-scale areas (barren land, mine spoils, abandoned smelter…).
After phytostabilization

## Slide 12
Mechanism
Phytostabilization
Before…
Method: Micro X-ray fluorescence
Kumpiene et al., Environ. Pollution, 2012.
After phytostabilization
As binding to poorly crystalline Fe oxyhydroxides
Notes: As is preferentially associated with poorly crystalline Fe-oxyhydroxides as opposed to crystalline Fe-(oxyhydr)oxide phases. Correlation maps of As:Fe reveal that As in the treated spoils is primarily contained in surface coatings as precipitates and sorbates. Arsenic binding with poorly crystalline Fe-oxyhydroxides diminishes its mobility. As speciation can be further characterized using micro-XRD and micro-EXAFS. One detailed example is shown below with Zn and Cu.

## Slide 13
  Phytostabilization
  Rhizofiltration
  Phytolixiviation
  Phytoextraction
  Phytovolatilization
Phytostabilization is a mature and cost efficient method when compared to other technologies.
Benefits:
Cons:
Not applicable to TMs readily translocated to leaves due to potential effects to the food chain.
Phytostabilization
Notes: Benefits: Phytostabilization is less disruptive and expensive than excavation, and is environmentally friendly. Metals are not « removed », the contamination has been mitigated.

## Slide 14
Rhizofiltration
Principle :
Refers to the use of plant roots to absorb, concentrate, and precipitate toxic metals from flowing water. In situ treatment.
Application :
Industrial wastewaters, surface runoffs from mines, groundwaters…
Pilon-Smits, Ann. Rev. Plant Biol., 2005.

## Slide 15
pH 3.08
2 FeS2 (s) + 7 O2 + 2 H2O → 2 Fe2+ + 4 SO42- + 4 H+ (1)
Fe2+ + ¼ O2 + H+ → Fe3+ + ½ H2O (2)
Fe3+ + 3H2O → Fe(OH)3 + 3H+ (3)
Oxidation of pyrite
Ore = CuFeS2
(chalcopyrite)
CuSO4.n(H2O)
Rhizofiltration
Example :
Acid mine drainage (AMD)
Mamut mine, Malaysia
Notes: Coal also contains pyrite. About half of the coal mine discharges in Pennsylvania have pH under 5.

## Slide 16
6.5 Mt/yr => 160 Mt total
Rhizofiltration
Slag heap
Slag heap
Example… to not follow
Notes: Paddy fields are heavily contaminated by Cu leached from the mine spoil. Solution => Belt of constructed wetland, semi-natural marsh or swamp to contain contaminants. Wetland sediments are generally anaerobic below a thin oxidized surface layer and contain organic carbon for microbial growth. The anoxic zone of the sediments provide conditions which favor microbial and chemical reducing processes, transforming iron and sulfates to hydrogen and sulfides (=> immobilization of TMs)

## Slide 17
Cu
0.6 mm
Rhizofiltration
Cu is associated with Fe and Mn (oxyhydr)oxides, clays, detrital organic matter, and roots.
6.5 Mt/yr => 160 Mt total
Slag heap
Slag heap
Example… to not follow
Micro X-ray fluorescence
Mn oxides
(phyllomanganates)
Fe oxides
Rice root
Notes: Cu is everywhere, associated with almost all organic and inorganic constituants. Other techniques can be used to characterized the TMs speciation => micro-XRD, micro-EXAFS. One example detailed below.

## Slide 18
6.5 Mt/yr => 160 Mt total
Rhizofiltration
… to follow
Slag heap
Slag heap
Example… to not follow
Constructed wetland
Increase of pH by microorganisms and root activity, and possibly with carbonate amendments.
Organic-rich substrate which fixes TMs.
Wetland sediments are generally anaerobic below a thin oxidized surface layer.
Marchand et al., Environ. Pollution, 2010.

## Slide 19
Phytotechnologies
  Phytostabilization
  Rhizofiltration
  Phytolixiviation
  Phytoextraction
  Phytovolatilization

## Slide 20
Phytolixiviation
Industrial and sewage sludge, soils and sediments in urbanized areas.
Phytorestore’s filter gardens
http://www.phytorestore.com
Principle :
2-step process. Removal of TMs by lixiviation and Retention by adsorption/precipitation. Ex situ treatment.
Application :
Phytolixiviation basin
Retention basin

## Slide 21
Phytolixiviation
Principle
Biofarm at Montereau, France
Phytolixiviation basins
Retention basin
Credit: http://www.phytorestore.com
Notes: Trucks unload the waste to be treated. The sludge is homogeneized. Treatment pots are floaded, and the lixiviates collected and purified in the retention basin, then re-injected into the circulating system in a closed-loop.

## Slide 22
150 - 3150
~ 350
~ 700
Zn
Cu
Pb
mg kg-1
Area: 1500 ha
Heavy metal concentration:
Until 1999…
Since 1999…
Truck farming activities
Only corn culture is permitted
Application :
Speciation of Zn and Cu in a land irrigated for 100 yrs. with Paris wastewater
Kirpichtchikova et al., GCA, 2006.
Notes: The Pierrelaye plain is about 30 km northwest of Paris (France), in the heart of an urban industrial suburb. From 1899 to 1999, truck farmers irrigated the plain regularly with untreated sewage water from Paris. Now the entire area is contaminated with a suite of heavy metals, dominated by Zn (1,103 mg/kg), Pb (535 mg/kg) and Cu (290 mg/kg). This kind of pollution is widespread because as industry and populations increase, and the availability of freshwater decreases, more and more farmlands are irrigated with wastewater and industrial effluents.

## Slide 23
500 µm
Zn
Cu
1 mm
Beam size: 5 x 5 mm
Micro X-ray fluorescence
Chemical Associations
Notes: Copper in the Pierrelaye soil is distributed between two morphological forms as seen in the XRF maps. Cu often decorates coarse organic particles with some recognizable structures from reticular tissue and also occurrs within the fine clayey matrix in areas that appeared featureless at low resolution, but showed organic particulate shapes at high resolution.
From chemical associations, at least two Cu species, one is organic + Zn-free, and the other is inorganic + Zn-bearing. One Zn species is common with Cu, and another is Fe-rich

## Slide 24
300 µm
500 µm
Zn
Cu
Beam size: 5 x 5 mm
1 mm
500 µm
Zn
Cu
Micro X-ray fluorescence
Chemical Associations

## Slide 25
500 µm
Zn
Cu
P
Zn
Beam size: 5 x 5 mm
1 mm
The Zn-Fe association likely corresponds to Zn-containing Fe (oxyhydr)oxide. What is its nature ?
Micro X-ray fluorescence
Chemical Associations
Notes: The Zn-P association likely corresponds to Zn-phosphate. The Zn-Fe association likely corresponds to Zn-containing Fe (oxyhydr)oxide. What is its nature? Response from micro-XRD.

## Slide 26
300 µm
Goethite (-FeOOH)
Identification of Mineral Species by m-XRD
Fe is speciated as goethite. Is Zn sorbed or incorporated into the goethite lattice?
The answer comes from m-XRD
Adsorbed Zn
Substituted Zn
Micro X-ray diffraction
Fe
Notes: This information is essential to devise how to remove Zn. If Zn is a surface complex, then it can be desorbed by a stronger complexant using acid-base reactions. Citrate would do it. If Zn is buried inside the goethite lattice, then the only way to get it out is to dissolve the host matrix, typically by reducing Fe(III) to Fe(II). This can be achieved by alternating nonflooded and flooded irrigation to simulate periodic redox conditions expected during heavy rainfalls and favorable to the reduction of ferric iron to ferrous iron.

## Slide 27
300 µm
Zn
k (Å-1)
k3(k)
61 % Phosphate + 38 % Willemite
R=0.35
Structural Forms of Zn at the Molecular Scale
The answer comes from Zn K-edge m-EXAFS
What is the proportion of each Zn species in the bulk soil ?
k3(k)
k (Å-1)
100 % Zn-substituted goethite
-(Fe,Zn)OOH
k (Å-1)
k3(k)
75 % Phyllosilicate + 26 % Goethite
R=0.39
Micro EXAFS
Notes: From visual comparison of elemental distributions on XRF maps, specific points-of-interest (POIs) are selected for micro-EXAFS measurements. Each point EXAFS spectrum ideally is from a pure Zn species identified from a spectral database. Otherwise, the nature and proportion of each Zn species in the mixture are determined from the reconstruction of the measured spectrum with a linear combination of reference spectra. The spectrum from the yellow spot is statistically identical to the reference spectrum for Zn incorporated into the goethite structure.

## Slide 28
k (Å-1)
k3(k)
Average Zn speciation
The answer comes from powder EXAFS
Bulk EXAFS
 … %
 … %
 … %
 … %
?
Goethite
Phosphate
Phyllosilicate
Willemite
k (Å-1)
k3(k)
Proportion of each Zn Species in the Bulk
Zn
Zn is predominantly bound to secondary minerals.
Precision :
10 % of total Zn
34 %
28 %
25 %
11 %
Micro EXAFS
Notes: Bulk Zn-EXAFS represents a weighted sum of all contributions around Zn from the complex assemblage of all Zn species in the sample. The percentage of each Zn species in the bulk sample is obtained by performing a linear fit of the POIs spectra to the bulk EXAFS spectrum.

## Slide 29
Objectives:
  To solubilize metals with natural organic acids (mostly citrate).
  To use plants to maintain the soil texture and to transform the residual fraction of metals into sparingly soluble forms.
Soil
Airduct
Porous substratum
Lixiviation outlet
Effects of chemical treatment and
rhizosphere activity on metal speciation
Pilot site
Phytolixiviation
Manceau et al., ES&T, 2008.
Notes: The phytoremediation experiment was conducted from May 2002 to September 2003. Holes 4 x 4 m2 at the surface and 40 cm deep were dug in the ground, lined with a permeable membrane, and configured with basal drains to collect percolating irrigation waters. Soil aeration was achieved with a horizontal network of pipes at the depth of the liner connected to the surface by vertical pipes (capped to prevent ingress of precipitation) at 9 locations per pot. Pots were filled with soil from the Pierrelaye plain, and vegetated with Iris pseudoacorus and Phragmites australis. The pots were exposed to natural precipitation and also irrigated to dissolve the TMs.

## Slide 30
Pilot site
Soil
Airduct
Porous substratum
Lixiviation outlet
Effects of chemical treatment and
rhizosphere activity on metal speciation
Phytolixiviation
Objectives:
  To solubilize metals with natural organic acids (mostly citrate).
  To use plants to maintain the soil texture and to transform the residual fraction of metals into sparingly soluble forms.

## Slide 31
Cu <1 %
Zn 38 %
Zn 0.01 %
Cu 0.03 %
Only a small fraction of Cu is lixiviated. Why?
Atomic fraction of metal exported (%)
5 mg kg-1 ≤ [Cu] ≤ 30 mg kg-1 DW
Micronutrient Cu
Accumulation in shoot ?
Modification of metal speciation in the rhizosphere
Solubilization ?
What is the form of metals after treatment ?
Notes: A large fraction of Zn was lixiviated, but not Cu, although it is phytotoxic. Why? The concentration of nutrient copper falls between 5 and 30 mg kg-1 dry weight (DW) in vegetative tissues. When in excess, copper can catalyze the production of hydroxyl radicals, with subsequent damage to macromolecules involved in the production (chloroplasts) and storage (mitochondria) of energy, to protein synthesis, and to biomembranes through the peroxidation of unsaturated fatty acids. Because Cu is phytotoxic, how did the plants detoxify it to “deal with it”?

## Slide 32
Resolution: 5 x 5 mm
Phragmites australis
Central cylinder (stele)
Cortex
Aerenchyma
Endodermis
Epidermis
Zn Cu Ca
endomycorrhizae
Manceau et al., ES&T, 2008.
Most of Cu is located in the cortex of roots. What is its form ?
Rhizosphere of Phragmites
What is the form of metals after treatment ?
Notes: Micro-fluorescence map. Cu is located in the cortex, composed of parenchymatous cells. No Cu is present in the central vascular cylinder from the stele that contains the vascular bundles known to translocate micronutrients to reproductive and photosynthetic tissues. Cu is excluded in the roots to protect phytosynthetic and reproductive tissues from the shoot. How is it detoxified?
Many wetland species have porous roots (aerenchyma tissue) for the supply of oxygen for root respiration

## Slide 33
Resolution: 5 x 5 mm
endomycorrhizae
k3(k)
µ-EXAFS
k (Å-1)
Cu métallique
µ-XRD
The answer comes from m-diffraction and m-EXAFS
Cu is detoxified as copper metal.
Cu°
Zn Cu Ca
Phragmites australis
Notes: Divalent Cu is detoxified as elemental Cu. By microorganisms or by the root physiological activity?

## Slide 34
Zn Cu Ca
Iris pseudoacorus
Optical image
Resolution: 8 x 8 mm
Hypha
ectomycorrhizae
What is the form of metals after treatment ?
Rhizosphere of Iris
Micro X-ray fluorescence
Cu2+ is reduced to Cu° by symbiotic mycorrhizae.
Notes: Response: Mycorrhizae do the job. The XRF map of the Iris rhizosphere is speckled with hot-spots of Cu grains ranging from about 5 to 20 microns in size The main roots and rhizome of iris do not contain detectable Cu grains, but in the surrounding soil Cu grains formed aligned features associated with Ca, suggesting a biological link. When viewed under an optical microscope the Cu spots occurred along the direction of filamentous and ramified organic structures, similar to root hairs or hyphae from ectomycorrhizal fungi. Fungal forms are more likely because mycorrhizal hyphae generally are anastamosing, whereas root hairs are not.
By analogy, Cu grains in the cortex of P. australis also may have been formed by mycorrhizae since the roots of this plant are colonized by arbuscular endomycorrhizae in contaminated soils and sediments.

## Slide 35
Phytotechnologies
  Phytostabilization
  Rhizofiltration
  Phytolixiviation
  Phytoextraction
  Phytovolatilization

## Slide 36
Phytoextraction
To export TMs to the shoot.
Principle :
Application :
Decontamination of soils and sediments. In situ treatment.
Alyssum bertolonii
> 1 % Nickel
Ni
Metal hyperaccumulators

## Slide 37
Thlaspi caerulescens
Arabidopsis halleri
Astragalus bisulcatus
> 1 % Selenium
Metal hyperaccumulators
> 1 % Zn et 0.1% Cd
Pteris vittata
~1 % As
Phytoextraction
To export TMs to the shoot.
Principle :
Application :
Decontamination of soils and sediments. In situ treatment.

## Slide 38
~2% Zn
Arabidopsis halleri
(Thlaspi caerulescens)
Arabidopsis thaliana
(Thlaspi arvense – Field pennycress)
Zn-smelter ash
Zn hyperaccumulation and Cu tolerance in the Brassicaceae family.
Phytoextraction
Non-hyperaccumulator
Zn/Cd Hyperaccumulator
Hyperaccumulation is metal-specific (no known Cu-hyperaccumulator), depends on the metal homeostasis.
Example :
Manceau et al., Am. J. Sci., 2000.
Notes: Physiological control by the plant.

## Slide 39
Arabidopsis halleri
Arabidopsis thaliana
Phytoextraction
Non-hyperaccumulator
Hyperaccumulator
- Zn/Cd + Zn/Cd
Zn hyperaccumulation and Cu tolerance in the Brassicaceae family.
- Zn/Cd + Zn/Cd
Example :
Credit: Dr. Emiko Harada
Notes: Here experiment with Cd, but would work similarly with Zn.

## Slide 40
Metal storage and speciation in below-ground tissues
Phytoextraction
[Zn]=265 ppm
Non-hyperaccumulator
Zn
Cu
Where and how are Zn and Cu stored ?
[Cu]=68 ppm
[Zn]=200 ppm
[Cu]=15 ppm
T. arvense
5 mg kg-1 ≤ [Cu] ≤ 30 mg kg-1 DW
Micronutrient

## Slide 41
X-ray tomography
cortex
stele
Xyleme
sap
hair
200 mm
Phytoextraction
Zn stored in vacuoles as Zn-malate, and on cell walls as Zn-phosphate.
Cu stored on cell wall as Cu-histidine.
Manceau et al. , Metallomics, 2013.
Non-hyperaccumulator
T. arvense
Metal storage and speciation
Beam size 70 x 80 nm2
Pixel size 180 x 180 nm2
Notes: X-ray tomography and nano-XRF images of Cu and Zn in a secondary root of Thlaspi arvense. Left. Image from the cortical tissue shows compartmentation of Cu on cell walls and Zn in vacuoles and on cell walls. Micro-XANES and micro-EXAFS show that the root restricts entry of Cu into the cytoplasm by chelation to histidine on the cell wall (next slide), and Zn by sequestration on the cell wall and within the vacuole. Pixel size: 0.18 (H) x 0.18 (V) micron2. Right. Image from the stele with several protoxylem and metaxylem vessels with thickened walls encrusted with lignin. Cu and Zn occur on the cell wall and in the xylem lumen (with capture of the xylem sap). Pixel size: 0.2 (H) x 0.2 (V) micron2.

## Slide 42
Phytoextraction
Metal storage and speciation in below-ground tissues
bis(bidentate) chelate
Bidentate-tridentate chelate
bis(tridentate) chelate
Hydrophobe chain
Strong chelate
pH ≤ ~4.5
pH ≥ ~7
~5 ≤ pH ≤ ~6
Notes: The L-histidine ligand changes orientation with pH. Micro-XANES and micro-EXAFS show that Cu is stored on cell walls as a unique five-coordinate Cu(II)–bis(L-histidinato) complex with one L-histidine behaving as a tridentate ligand and the other as a bidentate ligand. Tridentate binding of Cu(II) provides thermodynamic stability (similarly to Cu-citrate) needed to protect cells against copper toxicity, and bidentate binding enables kinetic lability along the cell wall through protein-protein docking with the non-bonded imidazole group (hydrophobic chain providing an anchor to proteins through van der Waals interactions).

## Slide 43
X-ray tomography
cortex
stele
Xyleme
sap
hair
200 mm
Phytoextraction
Zn stored in vacuoles as Zn-malate, and on cell walls as Zn-phosphate.
Cu stored on cell wall as Cu-histidine.
Beam size 70 x 80 nm2
Pixel size 180 x 180 nm2
Non-hyperaccumulator
T. arvense
Metal storage and speciation
Manceau et al. , Metallomics, 2013.

## Slide 44
Leaf of Arabidopsis lyrata
Phytoextraction
Zn
K
Non-hyperaccumulator
Metal homeostasis in above-ground tissues
Sarret et al., New Phytologist, 2009.
15x15 mm2
Tolerance: Zn bound to phosphate in nerves, likely on cell walls.
A. halleri, leaf tissue
Zn-malate
A. lyrata, nerve
Zn-phosphate
Zn
K
Leaf of Arabidopsis halleri
Hyperaccumulator
Hyperaccumulation: Zn-malate complex, likely in vacuoles.
Notes: Zn partitioning between the veins and the leaf tissue.

## Slide 45
Phytoextraction
Hyperaccumulator
Zn
Non-hyperaccumulator
Zn
A. halleri
Zn phosphate
Zn malate
Zn phosphate
Metal storage and speciation in
plant tissues
Tolerance to Zn: accumulation on cell walls and in vacuoles from cortical root cells.
Resistance to Zn: hyperaccumulation in vacuoles of leaf cells.
[Zn]=~1%
[Zn]=~50 ppm
Zn phosphate
Zn malate
Notes: Tolerance = exclusion of TMs from the shoot. Metals are sequestered on the root cell walls and sometimes (Zn, Cd) also in the root (cortical) vacuoles. Hyperaccumulation: capacity of the plants to store Zn,Cd also in the leaf vacuoles.

## Slide 46
Phytotechnologies
  Phytostabilization
  Rhizofiltration
  Phytolixiviation
  Phytoextraction
  Phytovolatilization
Cross-disciplinary field:
Agronomy
Soil science
Bio(geo)chemistry
Environmental mineralogy
Plant biology
Plant genetics

## Slide 47
CH3
Hg
S
N
O
C-H
Phytovolatisation
Example :
Transpiration of Hg(0) by phytovolitalization.
MerB
MerA
Demethylation of Hg
operon
Barkay et al., FEMS Micobiol. Rev., 2003.
Notes: merB gene codes for the MerB lyase; merA gene codes for the MerA mercuric reductase.

## Slide 48
Phytovolatisation
Ruiz et al. Plant Physiol., 2003.
Hg as phenylmercuric acetate
merA/merB
Standard
Integration of the merA and merB operons into the chloroplast genome.
Notes: In plants, the primary target of Hg damage is the chloroplast; Hg inhibits electron transport and photosynthesis. The operon coding for mercuric ion reductase (merA) and organomercurial lyase (merB) is inserted into the chloroplast genome to prevent the pollen transmission of foreign DNA. The use of chloroplast (or mitochondrial) transformation to enhance phytoextraction/phytovolatisation is particularly beneficial because it prevents the escape of transgenes via pollen to related weeds.

## Slide 49
Conclusion
1- The phytotechnology employed depends on the nature of the trace metal, the material to be treated, and its future usage.
Credit: Dr. T. Kirpichtchikova

## Slide 50
2- Regulations are important because the « technology remedy » attenuates and rarely solves the problem completely.
Conclusion
Credit: Dr. T. Kirpichtchikova

## Slide 51
3- Importance of Education.
Thank you!
Conclusion
Credit: Dr. T. Kirpichtchikova
Notes: Importance of recycling to minimize waste.